# Tadarida-D User Manual

## Software Installation

To install Tadarida-D for Linux (64-bits), you must download:
https://github.com/YvesBas/Tadarida-D/archive/master.zip

For Windows (from Vista to 8.1), you must download:
https://github.com/YvesBas/Tadarida-D_forWindows/archive/master.zip

In both cases, decompresseddownloaded zip file contains two directories:
- Sources
- Install

Executing TadaridaD file from the install directory will start the software.

Under Linux, it may be necessary:
- to modify the properties of TadaridaD file to make it executable.
- to execute “export LD_LIBRARY_PATH=.”, before executing TadaridaD

## Build

If you wish to read and modify TadaridaD sources, and then build it, use “sources” subdirectory of the install download (see above).

These sources have been built with Qt 5.5 (note: they have also successfully been built with Qt 4.8 and Qt 5.7 on Windows)

You can download « community version » of Qt5.5 (https://www.qt.io/qt5-5).
You must check « Open source distribution under an LGPL or GPL licence »).
To run the build, you must:
(1) copy the files “libsndfile…” and “libfftw3f…”, from the install subdirectory (see above) into the directory containing the executable file.
(2) include Qt5 libraries directory ( […]\bin) in the system path.

You may build the project with the Integrated Development Environment « Qt Creator ».

If you build on linux using command line, you can proceed like this from the directory of the source files:
1. Launch : [full path of the directory…/gcc_64/bin of Qt]/qmake
2. Launch : make

## Software function
Tadarida-D has no graphic interface. It is designed to be executed by command line or to be controlled by another software. It can be executed on Windows or Linux.

### Input settings
Following settings are available to the user:
-t [n] allows to execute n parallel threads (1 by default)
Note that 1 thread consumes approximately 150 MB of memory.
-x [n] is the time expansion factor, either 10 (default) for 10-times expanded .wav files (most commonly used in bat monitoring or 1 for direct recordings).
-v [n] sets the list of features to be extracted on each detected sound events (2 by default, see appendix)
_f [n] set the frequency bands to be used; n = 2 allows to treat low frequencies (0.8 to 25 kHz) whereas n=1 (default) treats high frequencies (8 to 250 kHz). See below “shapesDetect” method description for more details.
-c gives compressed version of .ta output files, either .ta.gz (gunzip) format on Linux or .tac (7-zip) format on Windows
After these settings, must be mentioned either a directory path containing .wav files or a list of .wav files, to be processed. Relative or absolute paths can be used.
« .wav files » must be short. Accepted limit depends on sound file characteristics (between 6.4 and 12.8 seconds in high frequency (HF) mode, and between 32 and 64 seconds in low frequency (LF) mode).
This limit is necessary for memory consumption and performances of Tadarida-D and Tadarida-C. We recommand treating sound files of 5 seconds duration (or less).

Here, find some examples of command lines executing Tadarida-D:
>TadaridaD -t 4 -x 1 file1.wav file2.wav
>TadaridaD -t 4 wavfolder

New feature (05/2016 – version 2.1):
A " –r [n]" setting recently introduced allows Tadarida-D to handle both recording (thanks to sox toolbox available in both Linux and Windows) and processing at the same time. N is the number of “.wav” files to generate (duration : 5 seconds).
In that case, we can indicate:
-a [code] for the input sound alsa device name (default: hw:1,0)
-w to save .wav files (suppressed after processing by default)
In that kind of use, no input files or directories are given.
For the moment, this feature is only tested on linux.
Example : ./TadaridaD –r 1000 –a r2  records 1000 sound files of 5 seconds and treats them.

Other new feature :

## Outputs
In a « txt » subdirectory, a «.ta » file appears for each .wav file. In a simple tab separated text format, you will find all the features extracted from the detected sound events (DSEs). First line gives the column headers, and each following line the value of each features for each sound event detected (basically, one line per DSE).
First columns are:
Filename: name of .wav file simple tab separated text format
CallNum: sound event identifier (integer)
Version: detection process version (see below)
FileDur: .wav file duration
SampleRate: .wav file sample rate
Following columns give features computed for each DSE (see below)
These files form the input of the classification process performed by Tadarida-C where the features are traduced to species identification through a Machine Learning process (See Tadarida-C manual).

Potential errors source are stored in "error.log" file (or “error[thread number].log” if several threads are executed) within the “log” subdirectory of Tadarida-D.

## Architecture:

TadaridaD is a non-graphical application to be executed from the command line in scripts, particularly on servers.
This application handles the sound events detection and features extraction, it is structured around 4 classes:

### DetecLaunch (main class)

The constructor operates the input parameters: directories of .wav files to process, number of threads to be executed, etc.

The process first distributes .wav files among the threads. Next, variables that will be used by the threads are initialized (to manage the variables that do not support multithreading) and the threads created (objects of Detec class) with the necessary settings, and then executed.

### Detec (thread treatment)

The object of Detec class retrieves provided settings and creates the object of DetecTreatment class that will handle the output processing (generation of features tables).
The run() method (executed by pdetec [i] -> start () ;) organizes treatment.
It calls for each .wav file to be processed, the treatOneFile method, which launches CallTreatmentsForOneFile(...) method of DetecTreatment class.
Note that the division of tasks between the Detec and Detectreatment classes avoid a duplication of code in the DetectTreatment class between Tadarida-D and Tadarida-L projects (see below).

### Classe DetecTreatment

After initialization, the CallTreatmentsForOneFile method handles the processing of each .wav file by successively calling the following methods:
#### openWavFile and computeFFT

These first two methods basically read .wav files and compute from it a time-frequency matrix using Fast Fourier Transformation (FFTW3 library).
FFT window size is set according to sample rate in order to get the most possibly constant frequency and time resolutions: respectively 0.2-0.4 ms and 0.6-1.2 kHz in HF mode, and 2-4 ms and 60-120 in LF mode.
FFT overlap is by default set to 75 % as an optimal trade-off between the amount of information collected and the computing speed.

#### correctNoise

This pre-processing step consists in two successive treatments: ignoring silence and frequency equalizing.
Ignoring silence consists in detecting periods in .wav files when no acoustic signals are recorded. This commonly happens when recording the output of some ultrasound detectors involving a trigger (e.g. Pettersson D240X©), but can also happens with any recorder when for example the microphone is accidentally unplugged. Note that periods when microphone output is recorded without any source of sound are not considered silence and thus are not ignored since they can provide good information on background noise level (see below).
Frequency equalizing is performed by substracting to each frequency line in the matrix its proper noise floor (5%-quantile in amplitude). This simple operation has strong consequences for sound event detection and several advantages:
It usefully reduces biases generated by heterogeneity in recorders output, especially gain and variable microphone sensitivity across frequencies, and thus makes Tadarida-D functional over a wide range of recorders.
It erases narrowband electronical noise without any loss of hearable sound events.
It separates sound events even when a chorus of individuals produce constantly a large amount of amplitude on a frequency band (a common situation with insects)

#### shapesDetects

This method determines the detection of sound events. A detected sound event (DSE) is here defined as a set of elements of the frequency-time matrix and aims at isolating an acoustic signal in both frequency and time coming from a single acoustic source. The process follows an hysteresis function involving two amplitude thresholds:
- the high threshold first determines the presence of a DSE, i.e. every element of the matrix over this threshold are part of a DSE.
- the low threshold second determines the limit of DSEs. An element in the matrix is indeed part of a DSE if it meets the following conditions: being over this low threshold AND (being adjacent in rows (frequency band) to an element of the DSE OR being less than 5 columns (approx. 1.5 ms in HF mode and 15 ms in LF mode) away from an element of the DSE).

Authors found optimal values at 26 dB for the high threshold and 20 dB for the low threshold. These values produced very low rates of false positives (detection in the background noise) and false negatives (hearable sound event not detected).
Highest amplitude value among the elements within the DSE defines the master point. At this stage, sound events are filtered according to the frequency band chosen: 8 to 250 kHz for high frequency and 0.8 to 25 kHz for low frequency. Note that the high frequency range chosen covers every known vocalization of bats and bush-crickets and the low frequency range covers most other animal vocalization.

#### detectsParameter2 and saveParameters

These two method consist in the computing and saving of numerical features on each DSEs (269 in version 1, 151 in version 2). These features are stored in tables within specific .ta files (tab separated text format, Fig. 2). See Appendix for the definition of each numerical features. Note that some of these numerical features are based on proven methods in bioacoustics whereas the others are based on an empirical approach. Authors have indeed looked for the most discriminant features for the most problematic pairs of species (i.e. those with highest error rates, see below) and added some new custom features each time they were needed to improve classification.

## Appendix : features list

Name	Definition	Version / (1)
StTime	Start time of the detected sound event (DSE)	X
Dur	DSE duration	X
PrevSt	Time difference between starts of the DSE and the previous one	X
FMin	Minimum frequency	X
FMax	Maximum frequency	V1
BW	FMax-FMin	X
FreqMP	Frequency of the master point (i.e. single element with the highest amplitude)	V1
PosMP	Time Position of the master point (in fraction of the DSE duration)	X
FreqPkS	Frequency of maximum energy (frequency energy is here calculated as the sum of amplitude among single frequency bands)	V1
FreqPkM	Frequency of maximum energy (frequency energy is here calculated as the mean of amplitude among single frequency bands)	V1
PosPkS	Time position of the element with maximum amplitude at FreqPkS (fraction of the DSE duration)	V1
PosPkM	Time position of the element with maximum amplitude at FreqPkM (fraction of the DSE duration)	V1
FreqPkS2	Frequency of the element with maximum amplitude at PosPkS time.	V1
FreqPkM2	Frequency of the element with maximum amplitude at PosPkM time.	V1
PrevMP1	Time difference between master points of the DSE and the previous one	X
PrevMP2	Time difference between master points of the DSE and the previous one whose master point is between FMax and FMin, and conversely its FMin-FMax interval contains FreqMP of the current DSE	X
NextMP1	Time difference between master points of the DSE and the next one	X
NextMP2	Time difference between master points of the DSE and the next one whose master point is between FMax and FMin, and conversely its FMin-FMax interval contains FreqMP of the current DSE	X
Amp1	Average amplitude among time windows within the 1st quarter of the DSE	X
Amp2	Average amplitude among time windows within the 2nd quarter of the DSE	X
Amp3	Average amplitude among time windows within the 3rd quarter of the DSE	X
Amp4	Average amplitude among time windows within the last quarter of the DSE	X
NoisePrev	Average amplitude among the elements neighbouring the DSE on the left on a 3-element width (approx. 1 ms before)	X
NoiseNext	Average amplitude among the elements neighbouring the DSE on the right on a 3-element width (approx. 1 ms after)	X
NoiseDown	Average amplitude among the elements neighbouring the DSE on the top on a 3-element width (approx. 2 kHz above)	X
NoiseUp	Average energy among the elements neighbouring the DSE on the bottom on a 3-element width (approx. 2 kHz below)	X
CVAmp	Coefficient of variation of Amp1, Amp2, Amp3 and Amp4	X
Dbl8	Amplitude difference between the DSE and low-frequency noise (=everything below 8kHz)	X
Stab	An index of amplitude stability around the master point: average amplitude change between neighbouring elements within the DSE, inversely weighted by distance from Master Point	X
HeiET	Number of time windows within the DSE, whose cumulated amplitude exceeds 80% of the cumulated amplitude of the master point time window	X
HeiEM	Number of time windows within the DSE, whose mean amplitude exceeds 80% of the mean amplitude of the master point time window	X
HeiRT	HeiET divided by total number of time windows	X
HeiRM	HeiEM divided by total number of time windows	X
HeiETT	Number of time windows, after master point and within the DSE, whose cumulated amplitude exceeds 80% of the cumulated amplitude of the master point time window	V1
HeiEMT	Number of time windows, after master point and within the DSE, whose mean amplitude exceeds 80% of the mean amplitude of the master point time window	X
HeiRTT	HeiETT divided by total number of time windows	X
HeiRMT	HeiEMT divided by total number of time windows	X
MedInt	Median of intervals between DSEs of similar frequency bands (i.e. whose master point is within +/- 2 frequency bands around the current DSE master point, corresponding to an approx. 3 kHz interval)	V1
Int25	1st quartile of intervals between DSEs of similar frequency bands (i.e. whose master point is within +/- 2 frequency bands around the current DSE master point, corresponding to an approx. 3 kHz interval)	X
Int75	3rd quartile of intervals between DSEs of similar frequency bands (i.e. whose master point is within +/- 2 frequency bands around the current DSE master point, corresponding to an approx. 3 kHz interval)	X
RInt1	Int75 / Int25	X
IntDev	Median deviation from MedInt among the “similar frequency” (see MedInt above) intervals	V1
SmIntDev	Median deviation from Int25 among the half smallest “similar frequency” (see Int25 above) intervals	X
LgIntDev	Median deviation from Int75 among the half largest “similar frequency” (see Int75 above) intervals	X
VarInt	IntDev/MedInt	X
VarSmInt	SmIntDev/Int25	X
VarLgInt	LgIntDev/Int75	X
RIntDev1	LgIntDev/SmIntDev	X
EnStabSm	Average change of amplitude between adjacent elements on a square of 7 x 7 elements around the master point (~2 ms - ~5kHz)	X
EnStabLg	Average change of amplitude between adjacent elements on a square of 21 x 21 elements around the master point (~6 ms - ~11kHz)	X
HetX	Proportion of change of amplitude slope, among each set of 3 consecutive elements along the time axis.	X
HetY	Proportion of change of amplitude slope, among each set of 3 consecutive elements along the frequency axis.	V1
HetXr	Idem HetX but restricted to the 7 frequency bands around the master point.	V1
HetYr	Idem HetY but restricted to the 7 time windows around the master point.	X
HetYr2	Average amplitude difference between adjacent elements	V1
HetCMC	Proportion of consecutive time windows where average amplitude slope changes	X
HetCMD	Average difference of average amplitude between each pair of consecutive time windows	X
HetCTC	Proportion of consecutive time windows where cumulated amplitude slope changes	X
HetCTD	Average difference of cumulated amplitude between each pair of consecutive time windows	X
HetCMnP	Number of local average amplitude maxima among time windows	V1
HetCMfP	Density of local average amplitude maxima among time windows	X
HetCTnP	Number of local cumulated amplitude maxima among time windows	V1
HetCTfP	Density of local cumulated amplitude maxima among time windows	X
HetPicsMAD	Median interval between local average amplitude maxima among time windows	V1
HetPicsMALD	1st quartile of intervals between local average amplitude maxima among time windows	X
HetPicsMABD	3rd quartile of intervals between local average amplitude maxima among time windows	X
HetPicsMRBLD	HetPicsMABD / HetPicsMALD	X
HetPicsTAD	Median interval between local cumulated amplitude maxima among time windows	V1
HetPicsTALD	1st quartile of intervals between local cumulated amplitude maxima among time windows	V1
HetPicsTABD	3rd quartile of intervals between local cumulated amplitude maxima among time windows	X
HetPicsTRLBD	HetPicsTABD / HetPicsTALD	X
VDPicsM	Median deviance from HetPicsMAD among intervals between local average amplitude maxima among time windows	V1
VLDPicsM	1st quartile deviance from HetPicsMAD among intervals between local average amplitude maxima among time windows	V1
VBDPicsM	3rd quartile deviance from HetPicsMAD among intervals between local average amplitude maxima among time windows	V1
VDPPicsM	VDPicsM / HetPicsMAD	V1
VLDPPicsM	VLDPicsM / HetPicsMALD	X
VBDPPicsM	VBDPicsM / HetPicsMABD	X
VDPicsT	Median deviance from HetPicsMAD among intervals between local cumulated amplitude maxima among time windows	V1
VLDPicsT	1st quartile deviance from HetPicsMAD among intervals between local cumulated amplitude maxima among time windows	V1
VBDPicsT	3rd quartile deviance from HetPicsMAD among intervals between local cumulated amplitude maxima among time windows	V1
VDPPicsT	VDPicsT / HetPicsTAD	V1
VLDPPicsT	VLDPicsT / HetPicsMALD	X
VBDPPicsT	VBDPicsM / HetPicsMABD	X
Ramp_2_1	Ratio of average amplitude between the elements whose frequency is twice that of the DSE and those of the current DSE	X
Ramp_3_1	The same for triple frequency	X
Ramp_3_2	The same for frequency multiplied by 1.5	X
Ramp_1_2	The same for half frequency	X
Ramp_2_3	The same for frequency multiplied by 2/3	X
Ramp_4_3	The same for frequency multiplied by 4/3	V1
RAN_2_1	Ratio of cumulated energy between the elements surrounding (3 elements width) those whose / frequency is twice that of the DSE and the elements whose / frequency is twice that of the DSE	X
RAN_3_1	The same for frequency multiplied by 3	X
RAN_3_2	The same for frequency multiplied by 1.5	X
RAN_1_2	The same for half frequency	X
RAN_2_3	The same for frequency multiplied by 2/3	X
RAN_4_3	The same for frequency multiplied by 4/3	X
RAHP2	Ratio of average bandwidth between the first half before the master point of the DSE and the following. The first nine time windows are more weighted. For the second part, only the part not exceeding the quarter of the length of the first part after master point is counted before the master pointe	V1
RAHP4	Ratio of average bandwidth between the first quarter before the master point of the DSE and the following. The first six time windows are more weighted. For the second part, only the part not exceeding the quarter of the length of the first part after master point is counted	V1
RAHP8	Ratio of average bandwidth between the first 1/8 before the master point of the DSE and the following. The first four time windows are more weighted. For the second part, only the part not exceeding the quarter of the length of the first part after master point is counted	V1
RAHP16	Ratio of average bandwidth between the first 1/16 before the master point of the DSE and the following. The first three time windows are more weighted. For the second part, only the part not exceeding the quarter of the length of the first part after master point is counted	V1
RAHE2	Ratio of average amplitude between the first half of the DSE and the following. The first nine time windows are more weighted. For the second part, only the part not exceeding the quarter of the length of the first part after master point is counted	V1
RAHE4	Ratio of average amplitude between the first quarter of the DSE and the following. The first six time windows are more weighted. For the second part, only the part not exceeding the quarter of the length of the first part after master point is counted	X
RAHE8	Ratio of average amplitude between the first 1/8 of the DSE and the following. The first four time windows are more weighted. For the second part, only the part not exceeding the quarter of the length of the first part after master point is counted	V1
RAHE16	Ratio of average amplitude between the first half of the DSE and the following. The first three time windows are more weighted. For the second part, only the part not exceeding the quarter of the length of the first part after master point is counted	V1

‘X’ = versions n°1 and 2 - ‘V1’ = only version n°1
Following features are based on the link between two DSEs who could potentially be harmonics of the same DSE. The conditions for two DSEs to be potential harmonics are that both master points are included in the time duration of both DSE. For each DSE, both an upper harmonic (Hup_) and a lower harmonic (Hlo_) are searched for. If no match is found, corresponding features equal to 0. If several matches are found, the closest DSE in FreqMP is selected.
Hup_RFMP	Ratio of FreqMP between “potential harmonic” (see definition above) and the DSE	X
Hup_PosMP	Time position of the Master Point of the potential upper harmonic (fraction of the DSE duration)	V1
Hup_PosSt	Time position of the start of the potential upper harmonic (fraction of the DSE duration)	V1
Hup_PosEn	Time position of the end of the potential upper harmonic (fraction of the DSE duration)	V1
Hup_AmpDif	Amplitude difference between the DSE and its potential upper harmonic	X
Hup_RSlope	Ratio of MC_Slope (see below) between potential upper harmonic and the DSE	V1
Hlo_RFMP	Same parameters for potential lower harmonic	V1
Hlo_PosMP		V1
Hlo_PosSt		V1
Hlo_PosEn		X
Hlo_Ampdif		X
Hlo_RSlope		V1

Line-based features
At last, 5 linear descriptors of each DSE are drawn. They correspond of a subset of elements of the DSE basically drawing a line on the spectrogram

1)  	MC is the line of elements which have the maximum amplitude on each time window (note that these elements may not be adjacent on the spectrogram matrix).
2)  	StE is the starting edge of the DSE (elements forming the left edge of the DSE)
3)  	UpE is the upper frequency edge of the DSE
4)  	DoE is the lower frequency edge of the DSE
5)  	StC is formed by the first elements forming a local amplitude maximum on each frequency band (matrix line). In many cases, StC significantly better describes modulated signals than other line types, even in case of intense and numerous echoes.
Note that ending edge is not taken into account since it is mainly driven by the echoes and supposed to give little valuable information because of this.

Tableau 2

Suffix	Definition	CM	CS	CN	CO	CO2
_Dur	Duration				V1	V1
_FMax	Maximum frequency	V1	V1
_FMin	Minimum frequency	V1		V1
_BW	Bandwidth (FMax-FMin)	V1	V1	V1
_FPk	Frequency of maximum amplitude					V1
_FPkD	Difference of _FPk with previous DSE					X
_TPk	Time of amplitude peak (in fraction of line duration)					X
_Slope	Modulation Slope	X	X	X	X	X
_ISlope	1/Slope				V1	X
_HCF	Frequency of the point of maximum change of slope over/before FlF (see below). Calculated with a least square error from a two segments regression.	V1	V1	V1	V1	V1
_THCF	Time of the point which gaves “HCF” (in fraction of line duration)	X	X	X	X	X
_FlF	Frequency of the flattest part of the line (calculated on 5 consecutive time windows). If several frequencies get a 0 slope, FlF takes the value of longest null slope.	X	X	X	V1	V1
_LCF	Frequency of the point of maximum change of slope under/after FlF. Calculated with a least square error from a two segments regression.	V1	V1	V1	V1	V1
_UpSl	Slope of the upper part of the line (over HCF)	X	X	X	X	X
_LoSl	Slope of the lower part of the line (below HCF)	X	X	X	X	X
_StF	Start frequency (first element in time)	V1
_EnF	End frequency (last element in time)	V1
_StSl	Start Slope	X	X	X	X	X
_EnSl	End Slope	X	X	X	X	X
_FlSl	Slope at the FlF point	X				X
_FPSl	Slope at the point of maximum amplitude	V1	X	X	X	V1
_CeF	Half-time Frequency	V1	V1	V1
_5dBBF	Frequency of the farthest point before FPk and less than 5 dB below peak amplitude	V1				V1
_5dBAF	Frequency of the farthest point after FPk and less than 5 dB below peak amplitude	V1				V1
_5dBBW	Difference between 5dBBF and 5dBAF	X				X
_5dBDur	Time difference between 5dBBF point and 5dBAF point	X				X
SDC	Cumulated changes in frequency slope. Calculated as the sum of abs((f(x+1)-f(x) - (f(x)-f(x-1))) where (f(x) is the frequency of the element x of the line.	V1	V1	V1	V1	V1
SDCR	SDC / Dur	X	X	X	X	X
SDCRY	SDCR / BW	V1	V1
SDCRXY	SDCRY / Dur	X	X
SDCL	Cumulated changes in frequency slope of the part of the line before the first eventual ascent succeeding the master point	X	V1
SDCLR	SDCL / Dur	V1	V1
SDCLRY	SDCLR divided by frequency amplitude	V1	V1
SDCLRXY	SDCLRY / Dur	V1	V1
SDCLOP	Cumulated changes in frequency slope of the “main slope” of the line. The “main slope” is defined as the part of the line which contains the master point and has no change of slope direction.	X	X
SDCLROP	SDCLOP / Dur	X	X
SDCLRYOP	SDCLOP divided by frequency amplitude of the pan	V1	X
SDCLRXYOP	SDCLRYOP divided (a second time) by duration	V1	V1
SDCLWB	Cumulated changes in frequency slope of the part of the line between the middle between start and master point and the first eventual ascent after master point	V1	X
SDCLRWB	SDCLWB / Dur	X	V1
SDCLRYWB	SDCLRWB divided by frequency amplitude	V1	V1
SDCLRXYWB	SDCLRWB divided (a second time) by duration	V1	V1
SDCLOPWB	Cumulated changes in frequency slope of the part of the line between the middle of this pan before master point and the end of it	V1	V1
SDCLROPWB	SDCLOPWB / Dur	V1	V1
SDCLRYOPWB	SDCLROPWB divided by frequency amplitude	V1	V1
SDCLRXYOPWB	SDCLWB divided (a second time) by duration	X	V1
SDCL_DNP	SDCL divided by the number of changes of direction of the line (positive/negative)	V1	V1
SDCLR_DNP	SDCL_DNP / Dur	X	X
SDCLRY_DNP	SDCLR_DNP divided by frequency amplitude	V1	X
SDCLRXY_DNP	SDCLRY_DNP divided (a second time) by duration	V1	V1
ELBPOS	Duration of line to the moment where the line makes a “bend” divided by the duration of the line before the first eventual ascent of the line. A “bend” is defined as the first element x where the slope ratio between 3 elements before and 3 elements after x is under 0.6	X	X
ELBSB	Slope of the part of the line ending at the first bend determined by local slopes (ELBPOS)	X	X
ELB2POS	The same as ELBPOS, but the bend id determined by the global slopes before and after the bend	X	X
ELB2SB	Slope of the part of the line ending at the first bend identified by global slopes (ELB2POS)	X	X
RAF	Ratio of time windows average frequency before the master point and after	V1
RAE	Ratio of time windows average amplitude before master point and after	V1
RAFE	RAF + RAE	X
RAFP	Ratio of the sums of time window average amplitude before and after master point	V1
RAFP2	Ratio of the sums of amplitude before and after master point	V1
RAFP3	Ratio of the sums of time windows average amplitude weighted by amplitude (of the point of the line), before and after master point	X
SBMP	Slope between the beginning of the line and the master point	X
SAMP	Slope between the master point and the end of the line	X
SBAR	SBMP/SAMP	X